## Slide 1: 4.9 GHz National Plan Update
Ralph Haller, NPSTC Chair David Buchanan Chair, NPSTC Spectrum Management Committee
APCO International Annual Conference August 16, 2015

## Slide 2: 4.9 GHz Overview
Original rules were set in 2003.
The Federal Communications Commission Notice for Proposed Rulemaking (FCC NPRM) June 2012 sought comments on changing rules.
NPSTC submitted the 4.9 GHz National Plan Recommendations in 2013.
Actual FCC rule changes are to be determined.

## Slide 3: Original 4.9 GHz Bandplan
Eight 5 MHz Channels; Aggregation up to 20 MHz Allowed
4.94 GHz
4.99 GHz
Five 1 MHz
Channels
Five 1 MHz
Channels

## Slide 4: Original 4.9 GHz Rules
50 MHz of spectrum: 4.94-4.99 GHz
Eligibility: public safety
Uses envisioned: broadband hot spots, point-to-multipoint (PTM), secondary point-to-point (PTP)
Regional plans optional: fewer than 10 regions have developed plans
No formal frequency coordination
Each applicant can obtain PTM license covering its jurisdiction for full 50 MHz
  Intended to provide flexibility for temporary coverage of major event or incident

## Slide 5: FCC NPRM in 2012
Indicated FCC believes the 4.9 GHz band could be more heavily used.
Questioned whether the band should be opened for uses other than public safety.
Sought comments on appropriate frequency coordination procedures.
Invited input on how the 4.9 GHz band can be used to complement the 700 MHz Nationwide Public Safety Broadband Network.

## Slide 6: NPSTC 4.9 GHz National Plan Recommendations
Topics Covered in NPSTC National Plan Recommendations
Licensing approach
Frequency coordination
Eligibility of critical infrastructure industries (CII)
Recommended revised bandplan
Airborne/robotic uses

## Slide 7: NPSTC 4.9 GHz National Plan Recommendations
Noted in the NPSTC 4.9 GHz National Plan Recommendations, Final Report, October 24, 2013
“…lack of required regional planning or frequency coordination also imposes uncertainty …”
“Some public safety entities even hesitate to use the 4.9 GHz band because they view the structure to be too close to that of an unlicensed band and are concerned they will receive interference.”

## Slide 8: 4.9 GHz NPSTC Recommendation
Shared
CII/PS
Co-primary
Two 5 MHz
Channels
Air-to Ground &
Robotics
Five 1 MHz
Channels
Narrowband Backhaul
PTP
Five 1 MHz Channels
Public Safety General Use Some potential access by CII through MOUs w/ PS
Six 5 MHz Channels
4.94 GHz
4.99 GHz
Plan also includes provisions for channel aggregation
NPSTC Recommended Revised Bandplan

## Slide 9: Response to the NPSTC 4.9 GHz National Plan Recommendations
General support for the plan.
However, two jurisdictions with heavy 4.9 GHz use and their own regional plans raised concerns about:
  Local control
  Spectrum efficiency
  Impact on existing operations
  Cost to change any existing operations
NPSTC filed an ex parte letter with the FCC to address the concerns.

## Slide 10: Local Control/Regional Plans
  Fewer than 10 of the 55 regions filed plans.
  Current licensing process ignores regional plans. An applicant can apply for and obtain full 50 MHz over entire jurisdiction without notification to the region.
  The NPSTC plan recognizes different needs in different areas.
  The NPSTC plan can actually strengthen regional plans; it recommends a new 120 day window to file regional plans.

## Slide 11: Spectrum Efficiency
Current rules allow multiple licensees in the same area to have all 50 MHz.
The NPSTC plan would limit channel aggregation to 10 MHz, however:
  If 10 MHz does not work for a region, the provisions of the NPSTC plan would allow an RPC to specify greater aggregation in its plan.
An increasing number of 4.9 GHz applications are for point-to-point operations. The NPSTC plan proposes application of some Part 101 technical rules which increase channel reuse, and improve spectral efficiency.

## Slide 12: Disruption/Cost
If RPC plan includes provisions for aggregation greater than 10 MHz and is approved, changes should be minimal.
If a current 4.9 GHz system isn't compliant with the new rules, the NPSTC plan recommends a five year grandfather period before any changes to a system would need to be made.

## Slide 13: Wireless Broadband Trends
The NPSTC plan includes provisions for both robotic video and airborne video links, both of which have been requested by public safety entities.

## Slide 14: APCO 4.9 GHz Task Force
APCO established a 4.9 GHz Task Force in June 2015 to address several issues:
How to increase public safety use of the band
How to reduce barriers to use of 4.9 GHz for public safety
How to drive investment in the band by public safety users and manufacturers
Identify what Wi-Fi "types" of uses can be made within the 4.9 GHz Band
NPSTC representatives are part of the APCO Task Force
The Task Force has been active; targeting response near end of August.

## Slide 15: What’s Next?
Discussions with the FCC indicate a Further NPRM is likely.
  Specific rule changes are needed to implement the NPSTC 4.9 GHz National Plan Recommendations
Exact timing of Further NPRM is uncertain.
Stay tuned.

## Slide 16: Questions?
Support@npstc.org
(866) 807- 4755