## Slide 1
The member organizations of the National Public Safety Telecommunications Council are grateful to the Department of Homeland Security's Science and Technology Directorate, Office for Interoperability and Compatibility (OIC) and the
National Protection and Programs Directorate, Office of Emergency Communications (OEC)
Points of view or opinions expressed are those of the originators and do not necessarily represent the official position or policies of the U.S. Department of Homeland Security.
Datacast
Use of Digital Television Datacasting
for Public Safety Broadband Communications

## Slide 2: Contents
Communication gaps
What is Digital Television (DTV) datacasting?
How does it work?
Where is it used today?
Ongoing initiatives
Key points to remember
Questions / contact information

## Slide 3: Communication Gaps
Technology gaps
– Cellular failures when needed for data/video
•
•
•
Public congestion on cellular data
Cellular not resilient to weather or extended power outage Wireless priority service is voice only
– Wireless Priority Service
•
•
•
Not yet supporting data
Does not solve video streaming server limitations Will not avoid user unicast congestion
Collaboration gaps
25 Pearl Harbor “Planning deficiencies”
Same deficiencies found in reported testimony
•
•
•
•
•
Congressional 9/11 Report Katrina Report
Virginia Tech Shootings Report Deepwater Horizon Report Major UASI police chief issues
“Infinite bandwidth everywhere” not the solution
Need detailed scenario-based collaboration
Bridge Collapse:
Why Did Cell Phones Fail?
by Tom Conlon, posted Aug 4th 2007 at 11:03AM
Communications Networks Fail Disaster Area Residents
By Arshad Mohammed and Jonathan Krim Washington Post Staff Writers
Thursday, September 1, 2005; Page D1
Sandy Created a Black Hole of Communication
By: Jim McKay on January 28, 2013
# | Failure | # | Failure | # | Failure
1 | Organization | 9 | Attitude | 17 | Inspection
2 | Assumption | 10 | Imagination | 18 | Preparedness
3 | Omission | 11 | Communication | s 19 | Consistency
4 | Verification | 12 | Paraphrase | 20 | Jealousy
5 | Supervision | 13 | Adaptability | 21 | Relationship
6 | Alertness | 14 | Disclosure | 22 | Priority
7 | Complacency | 15 | Insight | 23 | Reporting
8 | Intelligence | 16 | Dissemination | 24 | Improvement
25 Delegation |  |  |  |  | 

## Slide 4: What is DTV datacasting?
Using the nation’s television transmitters to deliver real-time broadband content to our First Responders
No cellular
Any number of receivers
Mobile command center DTV receiver
First Responder and other organizations
School and other city campuses
DTV Station
Operations Center
Example datacast content
Helicopter or drone video
Audio from radio systems
Any MS Windows files, including imagery
Uplink content on two-way link
Acknowledge receipt
Request specific content
Push content to be datacast
DOWNLOAD
UPLINK
Control for who sees content
1
2
3
4
5
7
6

## Slide 5: How does it work?
Cities and states decide determine local, regional and statewide content priorities
Federal Agencies (Including DHS agencies)
State Agencies and Guard
County Agencies
Cities/Towns
Others
PBS Coverage
Aggregation Point
PBS and commercial coverage
Select DTV Stations
Uplink
Downlink

## Slide 6: How does it work?
Injecting encrypted video, voice or data content into existing resilient high- power TV transmitter’s broadcast stream
Operations Center
Multiplexer
To DTV
broadcast transmitter
Encrypted UDP IP packets are injected into available (unused) MPEG packets
DTV datacast now has
encrypted packets from
the Operations Center
embedded in the station’s
normal transmission
High-Definition/Standard-
Definition DTV feeds for regular station programming
DTV stream of MPEG packets
At DTV Station
User Datagram Protocol (UDP)
Datacast access server
File storage
IP encapsulator
Packet Identifier (PID)
MPEG video, audio, and data payload
Special
datacast PID
Encrypted video, voice
or data files and
notifications crawl from
Operations Center
Equipment added to TV station
2
1
3
4
5
6
7

## Slide 7: Where is it used today?
Eight years of operation for school security situational awareness in Clark County, Nevada
  Fifth largest school district in the U.S.
  12,000 video cameras spanning 370 K-12 schools
  Floor plans and other data updated on PBS DTV server each night
Three years in Tidewater Region for University security support
Three years of operation in the National Capital Region for U.S. Park Police et al major events on the National Mall
March 2014 deployment to WGBH Boston

## Slide 8: Ongoing initiatives
Houston public safety demonstration
Continuation of WGBH effort
NIJ-Johns Hopkins study
Statewide helicopter video solution
PBS Consortium for public safety
Datacast-LTE (FirstNet) Ipv6-integration

## Slide 9: Points to remember
Broadband communication gaps persist in our cities
DTV datacasting provides the most resilient existing broadband infrastructure
  Available in most cities today
  Encrypted video, voice and data files available 24X7
  Uses transmitted data packets with public safety or other content targeted to selected individuals or groups
  PBS stations offer unique cost-sharing opportunities
Two-way communications uses all other existing media, such as LMR voice, for uplink
No need to link disparate organizations IT networks together for two-way communications

## Slide 10: Questions / contact information
Robert I. (Bob) Desourdis, Jr. VP for Solution Architecture SAIC
Fairfax, Virginia
E: desourdisr@saic.com M: 202.345.9094
Mark O’Brien President and CTO SpedtraRep, Inc.
Chantilly, Virginia
E: mobrien@spectrarep.com M: 703.625.6462